## Slide 1: Ideas for a modern microwave translator architecture
Gary, K6mg

## Slide 2: What’s changed
The current translator was built in 2004, 17 years ago
  Microwave LO’s were expensive and hard to build
  Narrow BW filters, ~40khz, were only available at low frequencies
  Microwave filters required an IF of 100+ MHz for decent rejection
Now in 2021
  Microwave LO’s are cheap and easy!
  Integrated IQ mixers make IF and RF filters unnecessary

## Slide 3: Implications
In 2004
  Expensive uwave LO -> shared for receive and transmit -> low loss uwave transmission line required to tx and rx antennas more than 10’ apart in order to achieve >80db isolation
  Double conversion was required to achieve decent image rejection at uwave and active BW
Now
  Easy, cheap uwave LO -> separate LO’s for TX and RX -> TX and RX can now be connected at low frequencies
  High Q microwave filters are still hard -> IQ up/down converters are plentiful

## Slide 4: Receiver
DSP
processor
AD6IW
Synthesizer
&
reference
Streaming Data
HMC1113
AD8332
10 GHz

## Slide 5: Receiver Specs
1,8db NF
25 db image rejection, use low IF to put image <10368
100+ db dynamic range
1+ MHz BW
HMC1113 $40, AD8332 $10, DSP $20
AD6IW synthesizer $120

## Slide 6: Transmitter
DSP
processor
AD6IW
Synthesizer
&
reference
Streaming Data
HMC521
HMC952

## Slide 7: Transmitter SPECs
2w output
22 db image rejection
$50 in Analog Devices parts

## Slide 8: Translator thoughts
In band control, RSSI, AGC, Beacon (CW, SSB, FM, Digital) are all in SW
Transmit and Receive can be arbitrarily separated or co-located
  Co-location offers possible sharing of reference, synthesizer, DSP

## Slide 9: Some additional thoughts
IQ up/down converters are available for 1.2, 2.4, 3.4, 5.7, 10, 24, 47 and 80 GHz
  The higher bands include LO multipliers
A transceiver could be built sharing one AD6IW synthesizer and one DSP
  Add a touch screen for control and display
  Club project?